## Slide 1: Overview of Brazilian PT program Brazilian Experience Renata Cristina Messores Rudolf Laboratory of Molecular Biology, Microbiology and Serology (LBMMS)

## Slide 2
Panel production
Brazilian Rapid Test Continuous Quality Improvement
Overview of Brazilian PT program
Laboratory of Molecular Biology, Microbiology and Serology

## Slide 3
Free proficiency test for the public healthcare services
Continuous (long-term follow-up)
Educational character (non-punitive)
Evaluates each healthcare professional individually
Overview of Brazilian PT program

## Slide 4
Overview of Brazilian PT program
Registered Health Units: 1,773
primary health care units
specialized services
hospitals and maternity
indigenous health districts
laboratories
Health Professionals registered in the program: 7,288
Panels per round: 4,100
80% nursing professionals

## Slide 5
Panels production

## Slide 6
Overview of Brazilian PT program

## Slide 7
Overview of Brazilian PT program

## Slide 8
Overview of Brazilian PT program
Healthcare Professionals registered in the program: 7,288
Healthcare Professionals participating in the last round: 4,709
Some of them do not participate in the rounds due to:
vacation
maternity leave
retirement
leave due to health problems
health care units registration not updated
panels shipped and unused

## Slide 9
Theoretical rounds
Questionnaire on the execution of RT and procedures recommended in the Brazilian Diagnostic Technical Manuals
One per year
Overview of Brazilian PT program
30 days

## Slide 10
Overview of Brazilian PT program
Practice rounds
Twice a year
Execution of rapid tests for HIV, syphilis and hepatitis C vírus (simultaneously) with four panel elements.
30 days

## Slide 11
Dried Tubes Specimens (DTS)
Participants hydrate with PBS-TWEEN before use
Overview of Brazilian PT program
Practice rounds
A- instruction manual (mainly about the hydration process)
B- two results forms
C- metallic bag with hermetic closure (ziplock)
D- four serum or plasma samples with red dye (DTS methodology)
E- PBS-tween buffer
F- 0.5 mL pasteur pipette
G- silica sachet

## Slide 12
Overview of Brazilian PT program
Practice rounds
trypan blue dye
Adapted from Parekh et al, 2010 - green
A – Blood; B – Phenol Red + Water; C - Phenol Red + PBS; D – Erythrosine red; E – Eosin Y; F – Red food coloring powder; G – Liquid dye for paints (red and black); and H – Liquid dye for paints (red).

## Slide 13
Overview of Brazilian PT program
Practice rounds
Temperatures
2ºC a 8ºC
21ºC a 25ºC
37 ºC
42 ºC
Dry
Humid
Tested: 1, 7, 14, 21, 28, 30, 35 and 40 days.
Rapid tests
Dye approval
40-day stability

## Slide 14
Overview of Brazilian PT program
Practice rounds

## Slide 15
Overview of Brazilian PT program
Practice rounds
Positive
Positive
Anti-HIV Rapid Test
(RDT1)
Anti-HIV Rapid Test
(RDT2)

## Slide 16
Overview of Brazilian PT program
Practice rounds
Transport via Brazilian Post Office

## Slide 17
Overview of Brazilian PT program
Practice rounds
Evaluation criteria:
Each sample: 25 points
RT1 HIV: 70%
RT2 HIV: 30%

## Slide 18
Overview of Brazilian PT program
Practice rounds
EXCELLENCE: 100% agreement
APPROVAL: 70 to 99% agreement
DISAPPROVAL:
agreement less than or equal to 69%;
use RT kits with an expired kits, regardless of the score obtained when performing the tests;
use the same diagnostic kit for RT1 and RT2 for HIV, regardless of the score obtained during the execution of the tests
PARTICIPATION:
use rapid test kit for oral fluid such as RT2
do not perform RT2 for HIV on samples reactive in RT1 for HIV
use an HIV self-test kit such as RT1 or RT2
use DUO HIV/Syphilis kit as RT2 for HIV

## Slide 19
Round | EXCELLENCE | APPROVAL | DISAPPROVAL | PARTICIPATION
21EQA20 | 56,7% | 28,1% | 15,2% | 332 HP
22EQA21 | 63,9% | 24,5% | 11,6% | 310 HP
24EQA22 | 63,7% | 24,6% | 11,7% | 271 HP
26EQA23 | 57,3% | 30,4% | 12,4% | 498 HP
27EQA23 | 69,6% | 20,7% | 9,7% | 315 HP
29EQA24 | 68,3% | 23,4% | 8,3% | 376 HP
Overview of Brazilian PT program
Practice rounds - HIV
HP: healthcare professionals
84,8%
88,4%
88,3%
87,7%
90,3%
91,7%
perform RT2 for HIV on samples non-reactive in RT1 for HIV

## Slide 20
Round | EXCELLENCE | APPROVAL | DISAPPROVAL | PARTICIPATION
21EQA20 | 56,7% | 28,1% | 15,2% | 332 HP
22EQA21 | 63,9% | 24,5% | 11,6% | 310 HP
24EQA22 | 63,7% | 24,6% | 11,7% | 271 HP
26EQA23 | 57,3% | 30,4% | 12,4% | 498 HP
27EQA23 | 69,6% | 20,7% | 9,7% | 315 HP
29EQA24 | 68,3% | 23,4% | 8,3% | 376 HP
Overview of Brazilian PT program
Practice rounds - HIV
DISAPPROVAL:
agreement less than or equal to 69%;
use RT kits with an expired kits
use the same diagnostic kit for RT1 and RT2 for HIV
HIV positive sample
Positive
Positive
Anti-HIV Rapid Test
(RDT1)
Anti-HIV Rapid Test
(RDT2)

## Slide 21
Round | EXCELLENCE | APPROVAL | DISAPPROVAL | PARTICIPATION
21EQA20 | 56,7% | 28,1% | 15,2% | 332 HP
22EQA21 | 63,9% | 24,5% | 11,6% | 310 HP
24EQA22 | 63,7% | 24,6% | 11,7% | 271 HP
26EQA23 | 57,3% | 30,4% | 12,4% | 498 HP
27EQA23 | 69,6% | 20,7% | 9,7% | 315 HP
29EQA24 | 68,3% | 23,4% | 8,3% | 376 HP
Overview of Brazilian PT program
Practice rounds - HIV
HP:
healthcare
professionals
PARTICIPATION:
use rapid test kit for oral fluid such as RT2
do not perform RT2 for HIV on samples reactive in RT1 for HIV
use an HIV self-test kit such as RT1 or RT2
use DUO HIV/Syphilis kit as RT2 for HIV

## Slide 22
Round | EXCELLENCE | APPROVAL | DISAPPROVAL
23EQA | 20,2% | 64,7% | 15,1%
25EQA | 31,2% | 61,1% | 7,7%
28EQA | 7,6% | 66,7% | 25,7%
Overview of Brazilian PT program
Theoretical rounds - HIV
84,9%
92,3%
74,3%

## Slide 23
Practice rounds
Theoretical rounds
https://qualitr.paginas.ufsc.br/

## Slide 24
Scale up plans:
printing of the identification of the elements directly on the tubes (currently these are adhesive labels);
maintain actions to expand the number of professionals and services;
validation of the freezing of panel elements while maintaining the stability of the results (used successfully in round 29EQA24)
Overview of Brazilian PT program
4,100 panels: 16,400 tubes + 4,100 PBS-TWEEN

## Slide 25
aeq@aids.gov.br